## Slide 1
Performance Interfaces for Hardware Accelerators
Jiacheng Ma, Rishabh Iyer, Sahand Kashani, Mahyar Emami,
Thomas Bourgeat, George Candea
Notes: Hi everyone. I am Jiacheng, I am going to present the work “Performance interface for hardware accelerators” Today, this is a joint work at EPFL with Rishabh, Sahand, Mahyar, and my advisors, Thomas Bourgeat, and George Candea.

## Slide 2: HW Accelerators Are Everywhere
Machine learning
  TPU, NPU, NVDLA, VTA
RPC message serialization/deserialization
  ProtoAcc, Optimus Prime
Network packet processing
  Menshen
Bioinformatics
  Darwin
Multimedia
  Image/video encoder/decoder
TPU
VTA
ProtoAcc
Menshen
JPEG Decoder
Notes: Hardware accelerators are becoming integral to boosting performance in various domains
For example, there are accelerators for speeding up machine learning, RPC message serialization and deserialization, network packet processing, bioinformatics, and many more for other domains.

## Slide 3: Problem: Accelerators Lack Performance Clarity
What are the inputs/outputs ?
Vendor answer:
What/How much it accelerates ?
Vendor answer:
?
Semantic interface
Accelerators can actually slow down your workload*
* Karandikar et al. "A hardware accelerator for protocol buffers." MICRO ‘21
Notes: (1 minute)
Now Imagine using one of those accel for your workload.
The first question you ask is what are its input and output. Fortunately, hardware vendors provide you that, it’s called a semantic interface.
Semantic interfaces are documentations that tell you how to use the accelerator.
The second, also the more important question you ask is what, and how much it accelerates, unfortunately, you won’t get an accurate answer
because vendors only provide numbers for benchmarks that may not be relevant to your workload.
If you decide to blindly offload tasks to this accelerator, (click) you might end up slowing down your system. Because accelerators can be optimized only for certain workloads and not suited for yours.
For example, Protoacc accelerator for RPC message serialization can be slower than a xeon cpu when the message is mainly long strings.

## Slide 4: Problem: Accelerators Lack Performance Clarity
Semantic interface
describes only the functionality
Performance interface* describes only the performance
* Iyer et al. ”Performance Interfaces for Network Functions” NSDI ‘22
What are the inputs/outputs ?
Vendor answer:
What/How much it accelerates ?
Our answer:
Semantic interface
Performance interface
Notes: To raelly get acceleration by using accelerators, engineers need “performance interfaces” which tell them how the accelerator performs under different workloads.
Performance interface is similar to semantic interfaces, but describes only the performance, instead of the functionality.
The idea of performance interface has been explored in the software domain mainly with the work PIX and CIFAR, today we will show a completely different methodology applied to the hardware domain.

## Slide 5
Tools can turn this IR into performance interfaces
Accelerators should ship with a precise performance IR
Accelerators must have performance interfaces
Notes: In this talk, I will convince you the following 3 statements,
First, accelerators must have performance interfaces,
Second, accelerators should ship with a precise performance IR.
Lastly, It’s possible to build tools that then transform this IR into performance interfaces.

## Slide 6: Outline
Performance interfaces
Performance IR
B
Notes: Next, I will show you what is a performance interface, and how to use it.
Then I will talk about a performance IR to represent performance of the HW and use it to derive a performance interface
Lastly, there is an easter egg we show at the end. So stay tuned.
(don't be serious)

## Slide 7: Performance Interface for ProtoAcc*
*ProtoAcc is for RPC message serialization/deserialization
Performance interface = program that …
takes the same input and
returns how long the accelerator
takes to process that input
A good performance interface is human-readable and executable
Notes: Let’s look one example to understand what a performance interface is.
On the right, I will show a performance interface for protoacc. Protoacc is an accelerator used for RPC message serialization and deserilazation.
A performance interface is a program, that takes the same input as the hardware accelerator, which is a series of messages.
And then returns how long the accelerator takes to process that input.
By the way, the internal logic of Protoacc is quiet complicated with massive parallelism.
However, we can still understand it’s performance by just reading the interface.
For example, reading the interface, we know that the cost of serializing all messages is the sum of serializing each message; we also know that the cost of serializing different message types are quite different and depends on how many bytes are in the message instance.
Interestingly, we also know that there is a fixed cost to pay, no matter how small the message is.
In just one minute, You can already understand so much about protoacc’s performance, and you have never used the accelerator before and didn’t do any benchmark.
A good performance interface is easy to understand by a human and also executable.
However, unlike the semantic interface, perfomrance interface may not be as precise as the real hardware. However, slight loss of accuracy will not affect it's usability.

## Slide 8: How to Derive Performance Interfaces ?
Cannot use the existing state of the art*
  Hardware is inherently parallel and asynchronous
Don’t want to extract from HW source code (RTL)
  RTL is the wrong abstraction (too low level)
Huge gap between human-readable interface HW execution model
There is a huge gap between
human readable interface and this execution model
* Iyer et al. ”Performance Interfaces for Network Functions” NSDI ‘22
Notes: So I showed you what is a performance interface, let’s talk about how to derive them.
We can’t use the existing state of the art because it is designed for SW. And hardware is inherently parallel and asynchronous, which is very different from the SW.
We don’t want to extract the interface directly from the HW source code or RTL, because RTL is wrong abstraction.
If you look at the human readable interface and this parallel execution of HW, there is actually a huge gap between them.

## Slide 9
RTL  performance IR  Interface
How to Derive Performance Interfaces ?
Performance IR
represents the performance-equivalent circuit that …
                finishes processing at the same clock cycle as the HW given the same input
doesn’t produce functionally meaningful results
HW
Performance
Functionality
performance IR
Performance
Functionality
Input
=
Notes: To bridge this gap, we propose peformance IR. We first, distill a Performance IR from the hardware source code or RTL, then transform this IR into the interface.
(click) This IR represents a performance equivalent circuit to the HW that will finish procesing at the same clcok cycle as the HW given the same input,.
Also this IR doesn’t produce functionally meaningful results because it’s functinally exquivalent.

## Slide 10
The Ideal Performance IR
Our performance IR = Latency Petri Net
Abstract
  Retains only performance-relevant information
Expressive
  Can represent all performance-relevant details
Formal
  Can be analyzed by tools
Notes: An ideal Performance IR should satisify the following requirements:
First it should be a higher-level abstraction of the HW that retains only the performance-relevant information, and discards everything else.
Second the PE-IR has to be expressive enough to represent all performance-relevant details.
Lastly, the PE-IR has to be formal such that analyzable by automated tools.
We came up with such an performance IR, called latency petri net, or LPN to represent the performance of RTL.

## Slide 11: Latency Petri Net ( LPN )
LPN is a parallel model close to HW
  with natural constructs to represent parallelism
  extends Petri nets
Arbitrary functions represent …
  performance
  data dependencies of parallel hardware modules
LPN is abstract, expressive and formal
Notes: LPN is a parallel model close to hardware with natural constructs to represent parallelism. LPNs are based on Petri nets with several extensions, and petri nets have a long history of being used to model parallel and asynchronous systems.
LPN allows arbitrary functions to represent performance and data dependencies of parallel hardware modules.
Finally LPN is abstract, expressive and formal.

## Slide 12: The Simplest LPN
Example LPN for a systolic array that multiplies
two x matrices (latency = cycles)
  Place <-> buffer
  Token <-> data
  Transition <-> compute
  Edge <-> wire
LPN represents performance with much less code than RTL
(<= 10% of RTL)
=
Accelerator | LOC of RTL | LOC of LPN
VTA | 6,628 | 506
JPEG | 7,003 | 109
Protoacc | 3,197 | 758
Darwin | 1,535 | 214
Menshen | 11,169 | 544
Notes: Now let’s look at the simplest LPN to understand its elements and how it works
The lpn, despite the simplicity, describes the performance of a matrix multiplication hardware module, this hardware module implements a systolic array and takes two matrices of size n by n and output the results after n cycles.
(click)This LPN has two places, which represent the hardware buffer to hold input or output data.
(click)This LPN also contains a transition that models performance aspect of hardware units. The delay function associated with the transition, computes how long the hardware would take to process the input stored in the input place. in this case, it computes the delay of the matrix multiplication given specific matrices.
finally this LPN has edges that connects the places and the transition.
(click)
Now we can run this LPN to get the performance of the HW.
First we feed the input matrices as to the hardware, to this LPN, the matrices are then converted into a token, that holds abstract features of the input, here, the token contains the property n stands for matrix dimension, and let's say the dimension is 400.
This transtion is now activated by this new token, which means it will consume the token after some delay as computed by the delay function which returns 400 in this case. So, the transition waits for the clock to tick 400 cycles, then consume the token and produce an empty token denoting the computation is done.
(click)
It’s obvious that this LPN uses much less code than the original systolic array implementation to just represent the performance.
In fact, this is true for all 5 real accelerators we constructed LPN for, where we use only 10% of code compared to the RTL.

## Slide 13: LPN Composition
=
=
Transitions operate in parallel just like the hardware
Notes: We can make this LPN more complicated by adding another simple LPN for the hardware component that loads the matrices into a buffer which can then be consumed by the matrix multiplication unit,
This new LPN works the same way as before, but the two transitions operate in parallel unless there are data dependencies, just like the hardware
This gives you a feel of how an LPN works, the LPN abstraction we described in the paper is much more powerful than what we describe here. Please look at the paper for more details if you are interested.

## Slide 14
HW engineers can produce an LPN in a few hours
Obtaining the LPN of an ML Accelerator
LOAD MODULE
FETCH MODULE
STORE MODULE
COMPUTE MODULE
LOAD MODULE
FETCH MODULE
STORE MODULE
COMPUTE MODULE
Notes: With all constructs provided by the LPN, we can turn a complex hardware design into LPN easily.
The example shown on the left is a real ML accelerator, VTA, it has fetch, load, compute and store module, to convert this hardware to LPN, we would create LPNs for the modules one by one and compose them together.
The final LPN is quite similar to the architectural view of hardware on the left, but with more details, furthermore, the LPN can acutally run and return the performance of the design, while the archi-diagram is not actionable at all.
Because LPN matches closely to hardware, it’s easy for HW engineers to produce an LPN by hand.
Based on our experiment, a hardware engineer could construction an LPN in a few hours after understanding the RTL for a non-trivial design, menshen, used in programmable switches, which has around 10,000 lines of Verilog code.

## Slide 15
LPNs are expressive
to capture all details related to performance
LPNs are accurate
with 1.7% average error across 5 real accelerators
Notes: LPN is also very expressive and we were able to capture different performance-related details for all 5 accel We contructed LPNs for.
The LPNs are also accurate with 1.7% average error across all 5 accelerators we evaluated.
The inaccurate part is a result of simplification from the RTL but not due to limitations of the LPN model.
(LPN is no more or less correct that the Verilog because they are writing by the same engineers, but in the future work, we envision building tools )

## Slide 16: Workflow to Derive Performance Interfaces
Accelerator
(e.g. Verilog RTL)
HW Engineer
SW Engineer
Transformation
Performance Interface
lpn2pi
LPN
Distillation
Notes: Remember, there is huge gap, a big wall, between parallel execution model for HW and readable, sequential performance interface.
(click) With LPN, we find a way to bypass this wall.
Furthermore, we fully close the gap, with a tool we built called lpn2pi , which transforms LPN into a performance interface

## Slide 17
lpn2pi: LPN  Performance Interface
LPN
Takes LPN and input space of interest
Produces a program that computes execution cycles for every input in that space
Aggregates delay functions into the program
  Accounting for the parallelism of transitions
  E.g., latency expression
Input features become free variables
  E.g., matrix dimension
lpn2pi
Perf.
Interface
Transformation
Input space
Performance interfaces are readable and accurate (< 20% avg error vs. HW)
Notes: (1 minute)
LPN2pi tekes an LPN and an input space of interest, then produces a program which we can a perfomrance interface that can compute execution cycles of the hardware for every input in that space.
LPN2pi aggregates delay functions in the individual transitions into Python code, in this process, it also take into account the parallelism and data dependencies of thos transitions
Lpn2pi uses input features or aggragation of those features as free variables in the interface, for the interface to be readable.
So, Lpn2pi produced interfaces are human readable, and the price we pay for readablity is that the interface is less accurate than the LPN, but the good news is it’s error is les sthan 20% on average
(1 minute)
LPN2pi tekes an LPN and an input space of interest, then produces an interface that can compute execution cycles of every input in that space.
LPN2pi aggregates latency expressions in the transitions, e.g., latency expression to𝑘𝑒𝑛.𝑛, after accounting for the parallelism, into sequential Python program
While doing so, LPN2pi, leverages abstract features of inputs, e.g., matrix dimension 𝑛 for the interface to be human readable.
Lpn2pi produced interfaces are accurate, for all 5 accelerators, the average error across benchmarks is below 20% compared to the HW.
Lpn2pi is less accurate than LPN because it’s an approximation of lpn and sacrifice accuracy for readability.

## Slide 18: Outline
Performance interfaces
Performance IR (LPN)
Beyond performance interfaces
Notes: We have looked at what performance interfaces are, we also saw the performance IR, LPN that makes deriving the interfaces possible
Now to this easter egg I have promised, which is we can actually do a lot more with LPN that go beyond performance interfaces, because LPN is a very efficient IR for performance

## Slide 19: lpn2sim: LPN  Performance Simulator
Accelerator
(e.g. Verilog RTL)
LPN
HW Engineer
SW Engineer
Distillation
lpn2pi
lpn2sim
Transformation
Perf.
Interface
Perf.
Simulator
1 - 3 orders of magnitude faster simulation than the state of the art
Notes: (1min)
We extended the transformation toolchain (click) with lpn2sim. That produces a fast performance simulator. The simulator produced is 1 to 3 orders of magnitude faster than a RTL simulator.
Workloads that actually depend on simulators, which normally take hours, now take seconds to run, so what used to be a batch mode workflow is turned into an interactive mode for the software engineers.

## Slide 20
lpn2smt: LPN  Performance Verification
LPN
SW Engineer
lpn2pi
lpn2sim
Perf.
Interface
Perf.
Simulator
lpn2smt
Perf.
Verification
lpn2smt: Formally verify performance bounds, find performance bugs
Accelerator
(e.g. Verilog RTL)
HW Engineer
Distillation
Transformation
Notes: We also developed lpn2smt, that produces SMT constraints from the LPN which can then be used to formally verify performance properties with a solver.
We used lpn2smt to prove upper bounds that a hardware jpeg decoder takes to do it’s job, and this is cruial for real-time systems that needs performance guarantee of accelerators
We also used lpn2smt to find a performance bug for the jpeg decoder itself. and found an under provision buffer, which improved the performance by 37% after fix.
We can even use lpn2smt to prove the maximum predication error a performance interface introduces compared to the LPN.
Please refer to the paper for more details.

## Slide 21
Tools can turn this IR into performance interfaces (and then some)
Accelerators should ship with a precise performance IR (LPN)
Accelerators must have performance interfaces
Notes: To conclude, this talk made the case that, accelerators lack performance clarity, and to fix that,
It must have perf interfaces.
They should ship with a precise performance IR, and we propose LPN for that,
Tools should then automatically transform this IR into performance interfaces and also many other useful represesntations.

## Slide 22
https://dslab.epfl.ch/research/perf
Performance Interfaces for HW Accelerators
SW Engineer
lpn2pi
lpn2sim
Perf.
Interface
Perf.
Simulator
lpn2smt
Perf.
Verification
Accelerator
(e.g. Verilog RTL)
LPN
HW Engineer
Distillation
Transformation
Notes: This work is part of a bigger project on performance interfaces for both sw and hw, and on the project website, you can find the LPNs and a fully open-source toolchain.
Thanks for your attention, I am happy to take questions now.

## Slide 23: Backup Slides

## Slide 24: Accelerators We Evaluated and Workloads
Accelerator | Domain | Workload
VTA | Deep Learning | Autotune ResNet-18
Protoacc | RPC message serialization | Hyperprotobench
JPEG | Image decoding | 60000 images
Darwin | Bioinformatics | 10 DNA test cases
Menshen | Programmable P4 network switch | Original testbenches

## Slide 25: LPN Errors Detailed

## Slide 26: lpn2sim Speedup

## Slide 27: Scalability of Tools
Tools | Step-1 | Step-2
lpn2pi | O(V+E) | O(V+I)
lpn2sim | O(V+E) | 
lpn2smt | O(V+E) | O(V+I)
V is number of places + transitions
E is number of edges
I is the size of the input